## Slide 1: DSP intro

## Slide 2: What is DSP?
The world of science and engineering is filled with signals: images from remote space probes, voltages generated by the heart and brain, radar and sonar echoes, seismic vibrations, and countless other applications.
Digital Signal Processing (DSP) is the science of using computers to understand these types of data. This includes a wide variety of goals: filtering, speech recognition, image enhancement, data compression, neural networks, and much more.
DSP is one of the most powerful technologies that will shape science and engineering in the twenty-first century. Suppose we attach an analog-to-digital converter to a computer, and then use it to acquire a chunk of real world data. DSP answers the question: What next?

## Slide 3: Linear Systems

## Slide 4: Definitions: Amplitude & Period
Continuous-time sine wave signal
x Amplitude

## Slide 5: Analog, Discrete or Digital ?
Analog signal  Sample  Discrete signal  Quantize  Digital signal
Need AN “Anti-aliasing filter” before sampling
Also needed before downsampling a digital signal.

## Slide 7: Systems & Signals
System
Input signal
output signal
x[n]  system  y[n]
System transforms input x[n] into output y[n]
Every system can be thought of as a filter, described by a transfer function, h[n]
Later we will discuss convolution, represented by ‘*’
  y[n] = x[n] * h[n]

## Slide 8: Terminology

## Slide 9: Smith: The Scientist and Engineer's Guide to Digital Signal Processing
PDFs of each chapter available from:
http://dspguide.com/
I will likely assign you readings from this book and base my lecture material on it.

## Slide 10: Why understand systems?
design a system to remove noise in an electrocardiogram
sharpen an out-of-focus image
remove echoes in an audio recording
measure distortion, interference
Understand data received from a radar or sonar system
The problem is to find the system that changes the transmitted signal into the received signal.
At first glance, it may seem an overwhelming task to understand all of the possible systems in the world. Fortunately, most useful systems fall into a category called linear systems. This fact is extremely important. Without the linear system concept, we would be forced to examine the individual characteristics of many unrelated systems.

## Slide 11: Sinusoidal fidelity
An important characteristic of linear systems is how they behave with sinusoids, a property called sinusoidal fidelity:
  If the input to a linear system is a sinusoidal wave, the output will also be a sinusoidal wave, and at exactly the same frequency as the input.
Sinusoids are the only waveform that have this property. For instance, there is no reason to expect that a square wave entering a linear system will produce a square wave on the output.
Although a sinusoid on the input guarantees a sinusoid on the output, the two may be different in amplitude and phase, e.g. a circuit can be described by its frequency response: graphs of how the circuit's gain and phase vary with frequency.

## Slide 12: Examples of non-linear systems

## Slide 13: What makes a system linear?
homogeneity
additivity
shift invariance

## Slide 14: LTI systems are commutative: order does not matter
Imagine a circuit composed of two stages, one for amplification, and one for filtering. Which is best, amplify and then filter, or filter and then amplify? If both stages are linear, the order doesn't make any difference and the overall result is the same.

## Slide 15: Multiplication by a constant is linear, but by another signal is not

## Slide 16: Superposition: the Foundation of DSP
Signals can only be combined is by scaling (multiplication of the signals by constants) followed by addition. Otherwise, system no longer linear.
This process of combining signals through scaling and addition is called synthesis.

## Slide 17: Superposition: the Foundation of DSP
Signals can only be combined is by scaling (multiplication of the signals by constants) followed by addition. Otherwise, system no longer linear.
This process of combining signals through scaling and addition is called synthesis.
Decomposition is the inverse operation of synthesis, where a single signal is broken into two or more additive components.
There are infinite possible decompositions for any signal (Fourier analysis gives us one possibility).

## Slide 18: Synthesis & decomposition

## Slide 19: Fundamental concept of DSP: Superposition
If system H transforms input signal x[n] into output signal y[n]
Then if we decompose x[n] into x1[n], x2[n], x3[n] and pass each of those individually through H, producing y1[n], y2[n], y3[n]
Then y1[n] + y2[n] + y3[n] = y[n]
So instead of trying to understand how complex signals are modified, we only need to know how simple signals are modified!

## Slide 20: Fourier decomposition

## Slide 21: time-shifting & time-reversal
revx = fliplr(x)

## Slide 22: Time scaling (changing frequency)

## Slide 23: Combining time operations:
What is x[-2n + 3] ?
Key is:
Shift
Flip
Scale

## Slide 24: Signals can be broken into Even and Odd components
MATLAB:
reversex = fliplr(x)
evenx = (x + revx)/2
oddx = (x – revx)/2

## Slide 25: Special signals: unit impulse & unit step functions
 Delta function
 Heaviside function

## Slide 26: unit step is running sum of unit impulse
Compare with: Continuous-time step function

## Slide 27: Unit impulse is difference of two unit steps
Continuous time
Discrete time

## Slide 28: You can make any signal of out delta functions

## Slide 29: Compose signal from sinusoids
Basis of Fourier Series/Transforms

## Slide 30: Sinusoids
Sine waves:
Mains AC
Signal generators
Oscillations in LRC circuits
Vibrations, resonance: e.g pendulums, musical instruments, bridges
electromagnetic waves

## Slide 31: Exponentials (real)

## Slide 32: Complex number review

## Slide 33: Complex numbers
“complex plane” or
“Argand diagram”

## Slide 35: Exponentials (complex) and relation to sinusoids

## Slide 37: Periodicity
Constant (DC, 0 Hz) signal is periodic with a sampling interval of 1T
For analog signal, T becomes 0, so

## Slide 38: Sinusoids are not generally periodic in discrete time
x[n] only periodic if is rational

## Slide 39: Non-periodic

## Slide 40: Computer Numbers: Integers

## Slide 41: Computer numbers: floating point (reals)

## Slide 43
Summary
Digital Signal Processing (DSP) is the science of using computers to understand signals and the linear systems that modify them.
DSP techniques are based on superposition, which assumes linear, time-invariant (LTI) systems.
LTI systems are homogeneous, additive, shift-invariant, commutative and have sinusoidal fidelity.
Signals can only be combined by scaling and adding (in that order). This is called synthesis (or composition).
Decomposition is the inverse operation of synthesis, where a single signal is broken into two or more additive components.
There are infinite possible decompositions for any signal (e.g. impulse, step, sine waves, even-odd, interlaced, ...).

## Slide 44
Digital signals
Basic operations include: time-shifting, time-flipping (reversal), time-scaling (in that order) – allows us to compute x[-2n+3] if we know x[n]
Special signals are: impulse, step, sine, exponential
Complex exponential (or complex sine) give rise to sine modulated by falling/rising exponential
Discrete-time sinusoids are not generally periodic unless we choose our sample times such that one period is some multiple of our sampling interval, e.g. if sine wave has a period of 10s and we choose T=1s, then this will be periodic. But typically naturally sine waves will have an irrational period, in which case it is hard to choose T.

## Slide 45
Impulse decomposition (one sample at a time)
Fourier decomposition (one frequency at a time)
The impulse decomposition is the basis of convolution.
The two fundamental decompositions

## Slide 46
(or “unit impulse”)
(or “kernel”)
Unit impulse is zero everywhere except at n=0
Impulse response tells us everything there is to know about a system

## Slide 47
Example:
Take a signal, x[n] = -3δ[n-8]
    (a=-3 at n=8; a=0 elsewhere)
Response to δ[n] is h[n]
Response to x[n] is y[n]=-3h[n-8]

## Slide 50
Length of convolution output
Length(y[n]) = length(x[n]) + length(h[n]) – 1

## Slide 51
End effect
At each end of signal there is only partial overlap between x[n] and h[n].
If h[n] has length M, first and last M-1 samples of y[n] are based on less information → transients.
Rule: embed the signal of interest in the middle of your discrete time series
Filtering is convolution

## Slide 52
Delta function
Passes the entire signal (all frequencies equally)

## Slide 53
Calculus
First difference / Discrete Derivative
Running sum / Discrete Integral
Recurrence relation
(recursion) or difference equation

## Slide 54
Adjacent positive values smooth data
Low Pass Filters

## Slide 55
High pass filters
Spike surrounded by negative values
High Pass Filters

## Slide 56
Causality
All real systems (e.g. analog electronics) are causal. They cannot respond to future values.
Digital systems(e.g filters) can be non-causal, because data can be stored first, processed later.
Causality

## Slide 57
Phase linearity
ZERO PHASE?
Think of cosine waves / even functions
For all frequency components, phase must be zero, else not symmetrical
ZERO PHASE?
Think of cosine waves / even functions
For all frequency components, phase must be zero, else not symmetrical
LINEAR PHASE
All frequencies shifted by same time, but that means a different number of wavelengths
Linearity

## Slide 58
Commutative (order of operations does not matter)
Associative
Distributive
Properties of convolution

## Slide 59
Central Limit Theorem
The result of many random processes tends to have a Gaussian (Normal) distribution

## Slide 60
Convolution – by hand, the long way

## Slide 64
Correlation
How related to signals are
Typically used for finding one signal within another longer one (matched filtering)
Cross-correlation: correlation between two different signals (can extract delay)
Auto-correlation: correlation between a signal and itself (useful for finding periodicities)

## Slide 65
Convolution by hand
x[-n]
h[n]
y[n]
x[n] = [2 3 -1 7]
x[-n] = [7 -1 3 2] (n=[-3 -2 -1 0])
h[n] = [-1 10 4]
y[n] = [-2 17 39 -5 66 28]
In MATLAB:

## Slide 66
3.3 The z-transform

## Slide 67
z-Transform: time-shifting
Take a signal:
  A[n] = [a0 a1 a2 … aN-1]
The z-transform is the polynomial:
Multiplying by z is the same as time-shifting by 1 sample:
because this is now the signal:
    [0, a0 a1 a2 … aN-1]
  In general, multiplying by zk delays a signal by k-samples.
  (z is just a symbol that represents a complex number, so a z-transform just means “complex transform”)
+1

## Slide 68
Multiplying two z-transforms
This is just the z-transform of the time sequence c[n] where:
Which is identical to the convolution formula:
Multiplying the z-transforms (polynomials) of two signals is the same as convolving them.

## Slide 69
Dividing two z-transforms
  B(z) = C(z) / A(z)
This is the inverse process of convolution: deconvolution

## Slide 70
Transfer function: poles and zeros
Since a z-transform is a polynomial, it has roots. In general a polynomial of order N has N complex roots, and can be factored into:
So we can also write the ratio of two z-transforms as:
This means that r(z) will become 0 when z is any of z0, z1, …, zN-1
and that r(z) will become ∞ when z is any of p0, p1, …, pM-1
The complex numbers z0, z1, …, zN-1 are the “zeros” of the function, r(z)
The complex numbers p0, p1, …, pM-1 are the “poles” of the function, r(z)
r(z) is called the discrete transfer function. It is the z-plane analog to the impulse response (which is defined for the time domain).

## Slide 71
Pole-Zero Plot
The unit circle
|z|=1
or
z = e-jω
where ω ranges from 0 to 2π

## Slide 72
Where is this going: filters
Any filter can be described by:
poles and zeroes (z-domain)
impulse response (time domain)
frequency response function (Fourier/frequency domain)
For continuous-time signals we use the Laplace transform / s-domain.
For discrete-time signals we use the z-transform / z-domain.
A perfect seismometer would respond equally to all frequencies. This is impossible. So seismometers are described by their transfer functions, given as a set of poles and zeros (e.g. SAC pole-zero files). From these poles and zeros we can work out the frequency response function (e.g RESP files).
Since seismometers deal with analog signals, we use Laplace transforms, not z-transforms. But for all the digital filters you will use (on a computer) it is more useful to know z-transforms.

## Slide 73
What is next?
The z-transform (i.e. discrete complex transform) is the discrete version of the Laplace Transform.
The Discrete-Time Fourier Transform (DTFT) is the special case of the z-transform evaluated along the unit circle, z=e-iw, i.e. a set of complex sinusoids.
The Discrete Fourier Transform (DFT) is a sampled version of the DTFT.
The Fast Fourier Transform (FFT) is an algorithm used to compute the DFT. This is what we use to do Fourier decomposition (decompose a complex signal into a discrete sum of different complex exponentials).
These, and their relation to Fourier Series (continuous periodic signals) and Fourier (Integral) Transform (continuous non-periodic signals), will be covered in detail later.